## Slide 1: Interfacing Tranceiver module with Arduino UNO and Beaglebone Black
Submitted by: Mohammed Abdul Muqeeth - C0751945
Group #: 5

## Slide 2: AGENDA
Task objective
Hardware used
Software used
Features of HC-12 Module
Pin configuration of HC-12 Module
Arduino UNO – HC 12 connection
BBB – HC 12 connection
Conclusion
References

## Slide 3: TASK OBJECTIVE
To establish a wireless communication between the Arduino UNO and Beaglebone Black.
Transmit the data from Arduino to BBB using wireless modules.
Protocol used : UART.

## Slide 4: HARDWARE USED
Arduino UNO
Beaglebone Black
HC-12 Module pair
MPU6050 gyroscope sensor
Jumper wires
Breadboard

## Slide 5: SOFTWARE USED
Arduino IDE
PUTTY
C language
Vi Editor
WinScp

## Slide 6: FEATURES OF HC-12 MODULE
Long distance wireless transmission (upto 1000m).
Working frequency : 433.4-473 MHz
Maximum transmitting power : 100mW
Built in MCU(stm8s003fs)
Ability to operate at higher baud rates

## Slide 7: PIN CONFIGURATION OF HC-12 MODULE

## Slide 8: STM8S003FS MICROCONTROLLER FEATURES
8-Bit microcontroller
8kb of lash RAM
Has 128 Bytes of EEPROM
Equipped with 10-bit ADC
Supports UART, SPI, I2C Communication

## Slide 9: ADVANTAGES OF HC-12 MODULE
Range is quite impressive (1km).
Compatible for industrial applications
Very handy in tracking related projects.

## Slide 10: ARDUINO UNO – HC 12 CONNECTION
ARDUINO UNO | HC 12 Module
PIN 10 | RXD
PIN 11 | TXD
VCC | VCC
GND | GND

## Slide 11: BBB – HC 12 CONNECTION
BBB | HC-12 Module
P9.24 | RXD
P9.26 | TXD
SYS_VCC | VCC
GND | GND

## Slide 12: CONCLUSION
A serial port communication between an Arduino UNO and BBB has been successfully established using a HC-12 Tranceiver module using UART communication protocol.

## Slide 13: REFERENCES
Understanding and Implementing the HC-12 Wireless Transceiver Module - Projects. (n.d.). Retrieved November 17, 2020, from Dejan, Zeeshan November 25, Dejan Nedelkovski November 26, Mark March 2, Dejan Nedelkovski March 6, Spencer March 18, . . . Name*. (2019, December 15). Arduino and HC-12 Long Range Wireless Communication Module. Retrieved November 17, 2020, from https://howtomechatronics.com/tutorials/arduino/arduino-and-hc-12-long-range-wireless-communication-module/
How to communicate two HC12 Module with Arduino. (n.d.). Retrieved November 17, 2020, fromhttps://create.arduino.cc/projecthub/franciscomoreirapcb/how-to-communicate-two-hc12-module-with-arduino-a0b5fa
By Trev, P. (2018, February 09). How to get UART serial ports working on the beaglebone black. Retrieved November 17, 2020, from https://electronics.trev.id.au/2018/02/09/get-uart-serial-ports-working-beaglebone-black/
Derekmolloy. (n.d.). Derekmolloy/exploringBB. Retrieved November 17, 2020, fromhttps://github.com/derekmolloy/exploringBB/tree/version2/chp08/uart

## Slide 14: APPENDIX